QUESTION BANK OF VLSI DESIGN

Q-1What is the active contact size in layout design rule?

- 1λ                        b. 2 λ                     c. 3 λ                         d.4 λ

Ans- 2 λ

Q-2  What is the minimum metal width in layout design rule?

- 1λ                        b. 2 λ                     c. 3 λ                         d.4 λ

Ans- 3 λ

Q-3  What is the minimum poly width in layout design rule?

- 1λ                        b. 2 λ                     c. 3 λ                         d.4 λ

Ans- 2 λ

Q-4 What is the distance between nmos and pmos transistor is determined by

- Minimum separation between p+ active area and p well.

- Minimum separation between n+ active area and n well.

- Minimum separation between n+ active area and p well.

- Minimum separation between p+ active area and n well.

Ans-   Minimum separation between n+ active area and n well.

Q-5  The distance between drain and source diffusion regions is called as

- Channel width.

- Channel  length.

- Channel

- None of the above

Ans- Channel  length

Q-6  What is meant by fan out of a logic gate?

- The same amount of cooling required by a gate.

- The physical distance between the output pins on device.

- Number of other  gates that can be connected to gate output.

- Number of other gates that can be connected to one of gate output’s.

Ans-  Number of other gates that can be connected to one of gate output’s.

Q-7 Silicon dioxide layer is used

- To protect the surface.

- It act as barrier to dopants.

- It act as insulating substrate.

- All of above.

Ans-  All of above.

Q-8 The threshod voltage is defined as

- The work function difference between gate and channel.

- Gate voltage component to change surface potential.

- Gate voltage to offset depletion region charge.

- All of above.

Ans-  All of above.

Q-9 In n-channel mosfet transistor

- The source is at higher potential than drain.

- The source is at lower potential than drain.

- The source is at same potential than drain.

Ans- The source is at lower potential than drain.

Q-10 In p-channel mosfet transistor

- The source is at higher potential than drain.

- The source is at lower potential than drain.

- The source is at same potential than drain.

Ans- The source is at higher potential than drain.

Q-11 Cmos technology is better than bipolar technology because

- High noise margin.

- Low packing density.

- Low input impedence.

- None of above.

Ans- High noise margin.

Q-12 The threshold voltage of nmos transistor is

- Positive quantity.

- Negative quantity.

- 0 voltage.

- 1 voltage.

Ans- Positive quantity.

Q-13 The threshold voltage of pmos transistor is

- Positive quantity.

- Negative quantity.

- 0 voltage.

- 1 voltage.

Ans- Negative quantity.

Q-14 The threshold voltage of nmos transistor is increased by

- Adding n-type impurities.

- Adding p-type impurities

- Cannot be increased.

Ans-  Adding p-type impurities

Q-15When input voltage is less than nmos threshold voltage then  following statement is correct

- Nmos transistor is in cut off region and pmos transistor is in linear region.

- Nmos transistor is in saturation region and pmos transistor is in linear region.

- Nmos transistor is in linear region and pmos transistor is in cut off region.

- Nmos and pmos transistors are in saturation region.

Ans-  Nmos transistor is in cut off region and pmos transistor is in linear region

Q-16 In cmos inverter, the maximum current is drawn when following condition is satisfied

- Nmos transistor is in cut off region and pmos transistor is in linear region.

- Nmos transistor is in saturation region and pmos transistor is in linear region.

- Nmos transistor is in linear region and pmos transistor is in cut off region.

- Nmos and pmos transistors are in saturation region.

Ans- Nmos and pmos transistors are in saturation region

Q-17 What is meant by the rise time of a waveform?

- Time delay from when the input step changes by 50% to when the output step changes by 50%.

- Time taken for the waveform to decrease from 90% to 10% of height of step.

- Time taken for the waveform to increase from 10% to 90% of height of step.

- Time taken for the waveform to increase from 10% to 90% of height of step.

Ans- Time taken for the waveform to increase from 10% to 90% of height of step.

Q-18 How much area is occupied by equivalent when depletion type load transistor area is negligible?

Ans-  4 times.

Q-19 If Kn=Kp and VT,N = VT,P then switching threshold of two input nor gate is?

Ans- Switching threshold of two input nor gate is VDD/2.

Q-20 What is the value of logic high and logic low output in transient analysis of cmos nor gate?

Ans- VOL=0V and  VOH=VDD.

Q-21 If series connected pmos transistor are represented by single pmos transistor then what will be the modified value of Kp?

Ans- kp/2

Q-22 In two input nor gate, if parallel connected nmos transistor are represented by single nmos transistor, then what will be the modified value of kn?

Ans- 2kn.

Q-23 What is the value of output voltage at switching threshold?

Ans- VA=VB=VOUT=VTH.

Q-24 What is minimum active contact spacing on same and different active region?

Ans-Minimum active contact spacing on same active region is 2 λ  and on different active region is 6 λ.

Q-25  In CMOS inverter

- N and P channel transistors are used in pairs.

- Bipolar and MOSFET transistors are used.

- No static current flows.

Ans- N and P channel transistors are used in pairs.